## Slide 1: Dual rotor physics model verification and 3D magnetic foam modelling
Jahnavi Sinha
Date: 5/9/22
TBD Project Picture

## Slide 2: Research Q: Using COMSOL to define dual PM rotor coil physics and verify 3D foam modelling
Aims:
Run 4 coil dual rotor model for ¼ period and 4 periods to verify current behavior in upper and lower rotors
Using 4 cell and 9 cell layer conductive foam models to characterize eddy currents and induced forces
Figure 1: Dual rotor model (left)
Figure 2: 3D coil model (right)

## Slide 3: Milestone 1a: Plotting 4 coil current results for upper and lower rotors at t = 0.025s
Upper rotor Lower rotor

## Slide 4: Milestone 2: Building 4-cell and 9-cell aluminium foam CAD models
4-cell model 9-cell model

## Slide 5: Milestone 2a: Magnetic flux density (4 cell model)
Plotting a cut plane at foam surface

## Slide 6: Milestone 2a: Magnetic flux density (9 cell model)
Plotting a cut plane at foam surface

## Slide 7: Milestone 2b: Lorentz force vs frequency plots for 4 and 9 cell foam models
Force peaks at ~1000 Hz then gradual plateau (same results for 9 cell model)

## Slide 8: Milestone 3: Observations and conclusions
Dual rotor model run for 4 coils, shows symmetric current behavior as PMs rotate (current in opposite directions for upper and lower rotors)
PMs rotate together in the same direction
Frequency domain study for 4 and 9 cell foam models
  Results make sense for 4 cell model
  Might need to verify results for 9 cell model

## Slide 9: Milestone 3a: Adjusting 4 cell layer foam model and running a frequency domain study
In progress
Yet to analyse frequency domain results
May need to rebuild mesh

## Slide 10: Milestone 3b: Adjusting 9 cell layer foam model and running a frequency domain study
No errors thrown on frequency domain even though domains are not selected
Nonsensical results for derived value tables